## Slide 1: Multicore Architecture & Programming
Sriram Kashyap - 2026

## Slide 2: Parallel Architectures

## Slide 3: Single Core CPU
Interface
Single Core CPU
DRAM / Peripherals
Registers
Compute Unit.
Super Scalar +
Vector Compute (SIMD)
Cache
Fetch + Instruction Cache
Decode + Branch Predictor
Dispatch + Reorder Buffer
Load
Store
Int
ALU
Float / SIMD ALU
Int
ALU
Int
ALU
Load
Inside an ALU
Implicit Parallelism: Execute scalar instructions ASAP (parallel / out of order)
Explicit Parallelism: Code includes explicit SIMD Operations
Frontend
Backend

## Slide 4: Multi Core CPU
Compute
Unit (ALU)
Registers
Cache
Interface
DRAM / Peripherals
CPU (1 core)
Interface
CPU (4 core)
DRAM / Peripherals
Compute
Unit (ALU)
Registers
L1 Cache
Compute
Unit (ALU)
Registers
L1 Cache
L2 Cache
Compute
Unit (ALU)
Registers
L1 Cache
Compute
Unit (ALU)
Registers
L1 Cache
Explicit Parallelism: User specifies multiple independent tasks
Shared Cache: Allows cores to run on shared datasets

## Slide 5: Digital Signal Processor
Interface
Single Core CPU
DRAM / Peripherals
Registers
Cache
Interface
Single Core DSP
DRAM / Peripherals
Registers
User-Managed SRAM
Compute Unit
Cache
Front
End
Load
Store
Int / Float
SIMD
Front
End
Load
Store
Int
SIMD Int / Float
Explicit Parallelism: Code includes explicit SIMD Operations
Specialized Core: Bigger SIMD / Load Store, Smaller Front End and Scalar
Non-Uniform Memory: User-managed high-speed on-chip memory

## Slide 6: Graphics Processing Unit
Registers
User-Managed SRAM
Texture Cache (Spatial locality for 1D / 2D / 3D arrays)
Front
End
Load
Store
Int
SIMD
Registers
User-Managed SRAM
Texture Cache (Spatial locality for 1D / 2D / 3D arrays)
Front
End
Load
Store
Int
SIMD
Registers
User-Managed SRAM
Texture Cache (Spatial locality for 1D / 2D / 3D arrays)
Front
End
Load
Store
Int
SIMD
Registers
User-Managed SRAM
Texture Cache (Spatial locality for 1D / 2D / 3D arrays)
Front
End
Load
Store
Int
SIMD Int / Float
Interface
Single Core CPU
DRAM / Peripherals
Registers
Cache
Front
End
Load
Store
Int / Float
SIMD
Wide Interface
DRAM / Peripherals
Big L2 Cache
Thread Dispatcher
GPU

## Slide 7: Neural Processing Unit
Interface
Single Core CPU
DRAM / Peripherals
Registers
Cache
Interface
Single Core DSP
DRAM / Peripherals
Registers
SRAM
Compute Unit
Front
End
Load
Store
Int / Float
SIMD
Front
End
Load
Store
Int
Implicit Parallelism: Compiler-driven & application-specific
Specialized Core: Large N-d matrix / tensor processing, systolic arrays…
Non-Uniform Memory: Compiler managed high-speed on-chip memory
Tensor Processors

## Slide 8: Compute Primitives
https://www.databasemart.com/blog/cpu-gpu-tpu

## Slide 9: Real computers

## Slide 10: Compute on a modern SoC
Interconnect
DRAM
Big CPU
Mid CPU
Mid CPU
Mid CPU
Tiny CPU
Tiny CPU
GPU
NPU
Audio DSP
Ambient CPU / DSP
Camera ISP
Secure CPU
…
Different processors specialized for different applications - for performance or power efficiency
Different stages of a single computation run on different processors

## Slide 11
Random Scary Block Diagram
(Snapdragon SoC)
The full chip has hundreds of components …
Dozens of programmable CPUs / DSPs …
Each running a different operating system and custom firmware.
Notes: Example camera capture

## Slide 12: Why Multicore?

## Slide 13: Parallel Compute
Compute Task
Compute Task
Compute Task
Compute Task
Single Core:
Multi Core:
Compute Task
Compute Task
Compute Task
Compute Task
Time
20 seconds
5 seconds

## Slide 14: Asynchronous Processing
File Read
Compute Task
File Read
Single Core:
Multi Core:
Time
Compute Task
File Read
Compute Task
File Read
Compute Task
20 seconds
15 seconds

## Slide 15: Amdahl's Law
Read Input
Compute Task
Write Output
1 Core:
2 Cores:
Time
Read Input
Write Output
Compute Task
Compute Task
∞ Cores:
Read Input
Write Output
20 seconds
16 seconds
12 seconds

## Slide 16: Example
#1: N-Body Simulation

## Slide 17: N-Body Simulation
Simulate gravity between ‘n’ point objects in 2D space:
In a for-loop, advance a time variable:
Calculate the force on each point due to every other point.
Calculate the acceleration due to this force on each point.
Calculate velocity of each point based on elapsed time.
Calculate position of each point based on elapsed time.
Force Due To Gravity between 2 masses at a distance:
force = Gravity_Constant x mass1 x mass2 / (distance ^ 2)
Equations of motion:
acceleration = force / mass
velocity = initial_velocity + acceleration * time_interval
position = initial_position + velocity * time_interval

## Slide 18: Coding N-Body Simulation
struct PointMass {
Point2D position, velocity;
float mass;
};
class ParticleSystem {
public:
// Compute the effect of all other
// points on point at `index`.
void CalculatePoint(int index, float timestep);
// Update the position of point at
// `index` based on current velocity.
void UpdatePoint(int index, float timestep);
// Simulate the whole system using a // time scaling factor `timestep`.
virtual void Simulate(float timestep);
protected:
std::vector<PointMass> data;
};
void ParticleSystem::CalculatePoint(int index, float timestep) {
PointMass& p = data[index];
// Calculate force on point p due to all other points.
Point2D net_force;
for (int j = 0; j < data.size(); ++j) {
Point2D vec = data[j].position - p.position;
float r = length(vec);
// Force due to a single point.
net_force += unit(vec) * p.mass * data[j].mass / (r * r);
}
// Update velocity based on force and timestep.
pi.velocity += net_force * timestep / p.mass;
}
void ParticleSystem::UpdatePoint(int index, float timestep) {
PointMass& p = data[index];
p.position += p.velocity * timestep;
}

## Slide 19: Parallel N-Body Simulation
void ParticleSystemOpenMP::Simulate(float timestep) {
#pragma omp parallel for
for (int i = 0; i < data.size(); ++i) {
CalculatePoint(i, timestep);
}
// Update results after all calculations are done. Could be parallel?
for (int i = 0; i < data.size(); ++i) {
UpdatePoint(i, timestep);
}
}
void ParticleSystem::Simulate(float timestep) {
for (int i = 0; i < data.size(); ++i) {
CalculatePoint(i, timestep);
UpdatePoint(i, timestep);
}
}
Sequential:
Parallel:
All results measured on Core i5-13600K (6 perf cores, 8 efficiency cores), running on Windows 11
Experiment Setup: 5000 points / 300 iterations / Measure Median time.
25 ms
2.7 ms
(9.3x)

## Slide 20: Understanding threads
std::thread (function, parameters)
Child Thread Execution
Main Thread Execution
thread::join
Waiting…
std::thread
std::atomic
Thread 1
Thread 2
std::atomic
Variable
Read and Decrement
Get Value
Set Value to 1
Value was 2
Return 2
Read and Decrement
Get Value
Set Value to 0
Value was 1
Return 1

## Slide 21: Understanding threads
std::mutex
Thread 1
Thread 2
std::mutex
Critical Code
Acquire Mutex
Mutex Acquired
Acquire Mutex
Execute Exclusive
Execute Completed
Release Mutex
Mutex Acquired
Execute Exclusive
Execute Completed
Release Mutex

## Slide 22: Explicit threading for N-Body Simulation
void ParticleSystemStdThread::Simulate(float timestep) {
int num_threads = scheduler::GetNumProcs(); // Query number of cores.
std::atomic<int> jobs(data.size()); // Thread-safe integer.
// Create and add threads to a pool.
std::vector<std::thread> threads;
for (int i = 0; i < num_threads; ++i) {
threads.emplace_back(WorkerFunction, this, &jobs, timestep);
}
// Wait for each thread to complete.
for (std::thread& t : threads) {
if (t.joinable()) t.join();
}
// Update results after all calculations are done.
for (int i = 0; i < data.size(); ++i) {
UpdatePoint(i, timestep);
}
}
void WorkerFunction(ParticleSystem* system, std::atomic<int>* jobs_ptr, float timestep) {
auto& jobs = *jobs_ptr;
// Parameter to control how many tasks
// each thread will do at a time.
constexpr int kJobSize = 4;
while(1) {
int end = jobs.fetch_sub(kJobSize);
int start = std::max(end - kJobSize, 0);
if (end < 0) return;
for (int i = start; i < end; ++i) {
system->CalculatePoint(i, timestep);
}
}
}

## Slide 23: Explicit threading for N-Body Simulation
void ParticleSystemStdThread::Simulate(float timestep) {
int num_threads = scheduler::GetNumProcs(); // Query number of cores.
std::atomic<int> jobs(data.size()); // Thread-safe integer.
// Create and add threads to a pool.
std::vector<std::thread> threads;
for (int i = 0; i < num_threads; ++i) {
threads.emplace_back(WorkerFunction, this, &jobs, timestep);
}
// Wait for each thread to complete.
for (std::thread& t : threads) {
if (t.joinable()) t.join();
}
// Update results after all calculations are done.
for (int i = 0; i < data.size(); ++i) {
UpdatePoint(i, timestep);
}
}
void WorkerFunction(ParticleSystem* system, std::atomic<int>* jobs_ptr, float timestep) {
auto& jobs = *jobs_ptr;
// Parameter to control how many tasks
// each thread will do at a time.
constexpr int kJobSize = 4;
while(1) {
int end = jobs.fetch_sub(kJobSize);
int start = std::max(end - kJobSize, 0);
if (end < 0) return;
for (int i = start; i < end; ++i) {
system->CalculatePoint(i, timestep);
}
}
}
2.75 ms
25 ms
3.13 ms
Sequential
OpenMP
std::thread

## Slide 24: Why is std::thread ‘a bit’ slower?
void ParticleSystemStdThread::Simulate(float timestep) {
int num_threads = scheduler::GetNumProcs(); // Query number of cores.
std::atomic<int> jobs(data.size()); // Thread-safe integer.
// Create and add threads to a pool.
std::vector<std::thread> threads;
for (int i = 0; i < num_threads; ++i) {
threads.emplace_back(WorkerFunction, this, &jobs, timestep);
}
// Wait for each thread to complete.
for (std::thread& t : threads) {
if (t.joinable()) t.join();
}
// Update results after all calculations are done.
for (int i = 0; i < data.size(); ++i) {
UpdatePoint(i, timestep);
}
}
void WorkerFunction(ParticleSystem* system, std::atomic<int>* jobs_ptr, float timestep) {
auto& jobs = *jobs_ptr;
// Parameter to control how many tasks
// each thread will do at a time.
constexpr int kJobSize = 4;
while(1) {
int end = jobs.fetch_sub(kJobSize);
int start = std::max(end - kJobSize, 0);
if (end < 0) return;
for (int i = start; i < end; ++i) {
system->CalculatePoint(i, timestep);
}
}
}
2.75 ms
25 ms
3.13 ms
Sequential
OpenMP
std::thread
Creating threads is not free

## Slide 25: Thread Pools
ParticleSystemStdThreadPool::ParticleSystemStdThreadPool() : pool_(scheduler::GetNumProcs()){}
void ParticleSystemStdThreadPool::Simulate(float timestep) {
int num_threads = scheduler::GetNumProcs();
std::atomic<int> jobs(static_cast<int>(data.size()));
for (int i = 0; i < num_threads; ++i) {
pool_.enqueue([&](){WorkerFunction(this, &jobs, timestep);});
}
pool_.wait_for_all();
// Update results after all calculations are done. Could be parallel?
for (int i = 0; i < data.size(); ++i) {
UpdatePoint(i, timestep);
}
}
void WorkerFunction(ParticleSystem* system, std::atomic<int>* jobs_ptr, float timestep) {
auto& jobs = *jobs_ptr;
// Parameter to control how many tasks
// each thread will do at a time.
constexpr int kJobSize = 4;
while(1) {
int end = jobs.fetch_sub(kJobSize);
int start = std::max(end - kJobSize, 0);
if (end < 0) return;
for (int i = start; i < end; ++i) {
system->CalculatePoint(i, timestep);
}
}
}
Create threads up-front to save some time. Now, jobs are ‘queued’ onto existing threads.
2.75 ms
3.1 ms
OpenMP
std::thread
2.70 ms
std::thread pool

## Slide 26: Performance is not a single number!
Histogram Plots
X Axis:
Time range in milliseconds
Y Axis:
Samples in each bucket
Run the experiment many times.
Sort the time taken into buckets.
Plot the buckets.

## Slide 27: Performance is not a single number!
230 Experiments
Completed in less than 2.8 milliseconds.
32 Experiments
Took longer than 4.6 milliseconds.

## Slide 28: Comparing techniques
OpenMP seems a lot worse.
Can we make it better?

## Slide 29: OpenMP Scheduling
1
Static Scheduling: #pragma omp parallel for
Dynamic Scheduling: #pragma omp parallel for schedule(dynamic)
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Job
Thread #1
Thread #2
Thread #1
Thread #2
1
2
3
4
5
6
7
8
Dynamic scheduling is better when jobs take variable time.
Although each job in n-Body simulation ‘should’ take the same time, variation in memory access, paging etc can cause practical differences for small workloads.

## Slide 30: Comparing techniques

## Slide 31: Multi Threaded Scaling
Scaling Notes:
First 6 big cores: Faster scaling.
Next 8 small cores: Slower scaling.
Beyond this: Some scaling, maybe due to additional threads hiding memory latency – but also possibly noise.
Chart: 
P50 | 25.0978 | 13.6722 | 9.3994 | 6.3411 | 5.2421 | 4.308 | 3.928 | 3.6423 | 3.4346 | 3.2541 | 3.0537 | 2.9223 | 2.7846 | 2.7869 | 2.7911 | 2.7917 | 2.7986 | 2.7918 | 2.8123 | 2.7908 | 2.7317 | 2.7024 | 2.708 | 2.7042 | 2.7045 | 2.7114 | 2.7063 | 2.7098 | 2.7247
Performance vs Thread Count
Number of Threads
Time in milliseconds
Chart: 
Scaling | 1 | 1.8357 | 2.6701 | 3.958 | 4.7877 | 5.8259 | 6.3895 | 6.8906 | 7.3073 | 7.7127 | 8.2188 | 8.5884 | 9.0131 | 9.0056 | 8.9921 | 8.9901 | 8.968 | 8.9898 | 8.9243 | 8.993 | 9.1876 | 9.2872 | 9.268 | 9.281 | 9.28 | 9.2564 | 9.2738 | 9.2619 | 9.2112
Scaling vs Thread Count
Performance Scaling
Number of Threads

## Slide 32: GPU – CUDA
__host__
void ParticleSystemCuda::Simulate(float timestep) {
cudaMemcpy(device_data_, data.data(), s_bytes_, cudaMemcpyHostToDevice);
int xdim = 32;
int ydim = (data.size() + xdim) / xdim;
CudaCalculatePoint<<<xdim,ydim>>>(timestep,
device_data_, data.size());
CudaUpdatePoint<<<xdim,ydim>>>(timestep,
device_data_, data.size());
// Wait for GPU to finish before accessing on host
cudaDeviceSynchronize();
cudaMemcpy(data.data(), device_data_, s_bytes_, cudaMemcpyDeviceToHost);
}
__host__
void ParticleSystemCuda::Initialize(int count, Point2D min, Point2D max, unsigned int seed) {
ParticleSystem::Initialize(count, min, max, seed);
s_bytes_ = data.size()*sizeof(PointMass);
cudaMalloc(&device_data_, s_bytes_);
}
__host__
ParticleSystemCuda::~ParticleSystemCuda() {
if (device_data_ != nullptr) {
cudaFree(device_data_);
}
}
__global__
void CudaCalculatePoint(float timestep, PointMass* data, int count) {
// Calculate the unique global index
int index = blockIdx.x * blockDim.x + threadIdx.x;
// Boundary check to prevent accessing memory out of bounds
if (index < count) {
PointMass& pi = data[index];
Point2D net_force; // calculate force on pi.
for (int j = 0; j < count; ++j) {
Point2D vec = data[j].position.Sub(pi.position);
float r_square = vec.SquareLength();
net_force = net_force.Add(vec.Scale( Gravity(pi.mass, data[j].mass, r_square)));
}
pi.velocity = pi.velocity.Add(net_force.Scale(timestep / pi.mass));
}
}
__global__
void CudaUpdatePoint(float timestep, PointMass* data, int count) {
// Calculate the unique global index
int index = blockIdx.x * blockDim.x + threadIdx.x;
// Boundary check to prevent accessing memory out of bounds
if (index < count) {
PointMass& pi = data[index];
pi.position = pi.position.Add(pi.velocity.Scale(timestep));
}
}
CPU
GPU
Each job processes just one data element.
CPU copies memory and launches jobs.

## Slide 33: GPU – CUDA
CPU
GPU
System RAM
Video RAM
Copy To GPU
GPU Compute
Video RAM
System RAM
Copy From GPU
Host (CPU)
Invoke ‘kernel’
Notify Finish

## Slide 34: GPU - CUDA
CPU Offloads work to the GPU and Waits
GPU Runs ‘Thousands’ of threads
Host (CPU)
Invoke GPU Kernel
Notify Finish
Th#1
Th#2
Th#3
Th#N
…
Th#4
Th#5
SIMT (Single Instruction Multiple Thread) Compute Core (32 Threads at a time)
SIMT Core
SIMT Core
…
SIMT Core
Hardware Dispatcher
…

## Slide 35: GPU - CUDA
‘Single Source’ authoring: C Program for CPU / GPU can be mixed in same files using special annotations.
__host__ : Traditional CPU function
__global__ : GPU Entry-point function. Called from CPU, parallelized across GPU cores.
__device__ : GPU internal function. Called from other GPU functions.
Function Name
Number of Threads
Arguments
Calling a __global__ function from CPU:
CudaUpdatePoint<<<xdim,ydim>>>(timestep, device_data_, data.size());
CUDA splits threads into <<<threads, blocks, grids>>> for ease of use in 2D / 3D computations.
There are limits on each dimension. N-Body is a linear (1D problem), so we use a reasonably large xdim, and based the ydim on that. We don’t need a z-dimension for our current problem.

## Slide 36: CUDA Performance
Chart: Performance comparsion - milliseconds
| latency_nbody_mt_openmp | latency_nbody_mt_std | latency_nbody_mt_stdpool | latency_nbody_mt_openmp_dynamic | latency_nbody_cuda
P50 | 2.7476 | 3.1294 | 2.7029 | 2.669 | 0.2807
P90 | 4.7112 | 3.41 | 2.807 | 2.7773 | 0.28791
P99 | 5.0692 | 4.925 | 2.9831 | 2.9499 | 0.36017
CPU: Core i5-13600K (6 perf cores, 8 efficiency cores)
GPU: nVidia GeForce RTX 5080 (10752 CUDA cores)
OS: Windows 11
9.5x
faster than Dynamic OpenMP
89x
faster than Sequential CPU

## Slide 37: CUDA Performance
void ParticleSystemCuda::Simulate(float timestep) {
cudaMemcpy(device_data_, data.data(), s_bytes_, cudaMemcpyHostToDevice);
int xdim = 256;
int ydim = (data.size() + xdim) / xdim;
CudaCalculatePoint<<<xdim,ydim>>>(timestep, device_data_, data.size());
CudaUpdatePoint<<<xdim,ydim>>>(timestep, device_data_, data.size());
cudaDeviceSynchronize();
cudaMemcpy(data.data(), device_data_, s_bytes_, cudaMemcpyDeviceToHost);
}
4%
2%
79%
15%
Percentage breakdown of time by stage
5000 Points: ~156 KB of data copied at each stage.

## Slide 38: CPU / GPU Scaling
Chart: Time (milliseconds) vs Problem Size (number of Points) - Linear Chart
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
OpenMP | 0.0043 | 0.0053 | 0.0085 | 0.0099 | 0.0096 | 0.0104 | 0.0117 | 0.0228 | 0.029 | 0.051 | 0.137 | 0.4854 | 1.8042 | 7.1564 | 28.5192 | 114.458
CUDA | 0.0199 | 0.0205 | 0.0208 | 0.0218 | 0.0219 | 0.0359 | 0.0375 | 0.0419 | 0.0719 | 0.0675 | 0.0833 | 0.1228 | 0.2487 | 0.4133 | 0.8968 | 3.3205

## Slide 39: CPU / GPU Scaling
Chart: Time (milliseconds) vs Problem Size (number of Points) – Log Scale Chart
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
OpenMP | 0.0043 | 0.0053 | 0.0085 | 0.0099 | 0.0096 | 0.0104 | 0.0117 | 0.0228 | 0.029 | 0.051 | 0.137 | 0.4854 | 1.8042 | 7.1564 | 28.5192 | 114.458
CUDA | 0.0199 | 0.0205 | 0.0208 | 0.0218 | 0.0219 | 0.0359 | 0.0375 | 0.0419 | 0.0719 | 0.0675 | 0.0833 | 0.1228 | 0.2487 | 0.4133 | 0.8968 | 3.3205
5x slower
34x faster

## Slide 40: Shared Memory Optimization
Th#1
Th#2
Th#3
Th#4
Read#1
Read#2
Read#3
Read#4
Compute
Compute
Compute
Compute
Write#1
Read#1
Read#2
Read#3
Read#4
Compute
Compute
Compute
Compute
Write#1
Read#1
Read#2
Read#3
Read#4
Compute
Compute
Compute
Compute
Write#1
Read#1
Read#2
Read#3
Read#4
Compute
Compute
Compute
Compute
Write#1
Example with 4 points and 4 threads
Th#1
Th#2
Th#3
Th#4
Read#1
Compute
Compute
Compute
Compute
Write#1
Read#2
Compute
Compute
Compute
Compute
Write#1
Read#3
Compute
Compute
Compute
Compute
Write#1
Read#4
Compute
Compute
Compute
Compute
Write#1
Shared Local Memory
Leverage ~48 KB local memory shared
between all threads
in a block.
Thread Execution
Thread Execution

## Slide 41: Shared Memory Optimization
__global__ void CudaCalculatePointShared(float timestep, PointMass* data, int count) {
__shared__ char shared_data_raw[256 * sizeof(PointMass)];
PointMass* shared_data = reinterpret_cast<PointMass*>(shared_data_raw);
int index = blockIdx.x * blockDim.x + threadIdx.x;
int tid = threadIdx.x;
Point2D net_force;
PointMass pi = (index < count) ? data[index] : PointMass{};
for (int i = 0; i < count; i += blockDim.x) {
if (load_index < count) { shared_data[tid] = data[i + tid]; }
__syncthreads();
if (index < count) {
int limit = min((int)blockDim.x, count - i);
for (int j = 0; j < limit; ++j) {
Point2D vec = shared_data[j].position.Sub(pi.position);
float r_square = vec.SquareLength();
if (r_square > 0.0f) {
net_force = net_force.Add(vec.Scale(Gravity(pi.mass, shared_data[j].mass, r_square)));
}
}
}
__syncthreads(); // Synchronize before loading the next tile
}
// Write final velocity update
if (index < count) {
pi.velocity = pi.velocity.Add(net_force.Scale(timestep / pi.mass));
data[index].velocity = pi.velocity; // or update back
}
}
Allocate local memory. This breaks
the problem into logical ‘blocks’.
Loop over each block.
Co-operatively read input data per block.
Move on to the next block.
Write the final accumulated result.
Local variable to accumulate result
across blocks.

## Slide 42: Shared Memory Optimization
Chart: CUDA Performance: Naive vs Shared Memory
| 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768
CUDA | 0.0685 | 0.0682 | 0.0832 | 0.1212 | 0.2477 | 0.409 | 0.8922 | 3.3213
CUDA_Shared | 0.0705 | 0.1039 | 0.1225 | 0.1488 | 0.2332 | 0.3208 | 0.5683 | 1.5218
2x faster

## Slide 43: Drawbacks of SIMT / SIMD
Toy variant of n-Body simulation to cause ‘code divergence’
Add a new parameter per point, to indicate that it is ‘frozen’ in space.
‘Frozen’ points effectively skip all computation on themselves.
Set every alternate point in the system as ‘Frozen’
Th#1
Th#2
Th#3
Th#4
Compute
Point #1
CPU Execution
Compute
Point #3
Compute
Point #5
Compute
Point #7
Compute
Point #9
Compute
Point #11
Compute
Point #13
Compute
Point #15
Th#1
Th#2
Th#3
Th#4
Compute
Point #1
GPU Execution
Compute
Point #2
Compute
Point #3
Compute
Point #4
Compute
Point #5
Compute
Point #6
Compute
Point #7
Compute
Point #8
Compute
Point #9
Compute
Point #10
Compute
Point #11
Compute
Point #12
Compute
Point #13
Compute
Point #14
Compute
Point #15
Compute
Point #16
CPU has per-thread control flow, and
efficiently skips frozen points.
GPU has per-thread control flow, and
efficiently skips frozen points.

## Slide 44: Drawbacks of SIMT / SIMD
Chart: CPU OpenMP Performance
| 0 | 1 | 4 | 8 | 16 | 32
nbody_mt_openmp | 28.6826 | 14.4364 | 14.4971 | 14.4112 | 14.2553 | 14.2323
Chart: CUDA Performance
| 0 | 1 | 4 | 8 | 16 | 32
nbody_cuda | 0.8966 | 0.8926 | 0.763 | 0.7847 | 0.7745 | 0.7693
X Axis:
0: No points are fixed (original problem).
1: Every alternate point is fixed.
4: First 4 points are fixed, next 4 are not …
8: First 8 points are fixed, next 8 are not …
16: First 16 points are fixed, next 16 are not …
32: First 32 points are fixed, next 32 are not …
Observations
CPU is 2x faster when half the points are skipped, regardless of the pattern.
GPU performance is same for ‘0’ and ‘1’ – indicating that SIMT block is unable to skip computation efficiently.
GPU performance improves from a block size of ‘4’, indicating that SIMT block has some optimization for this.
However, improved performance is barely 15%, because the problem is memory bound (entire point data are still read by active points).

## Slide 45: Links
https://github.com/sriramkashyap/MulticoreProgramming